## Slide 1
The applicability of analog/mixed signal devices in embedded systems increased
Sensitivity of analog parts to parameter deviations
Efficient methods for verification of system with parameter deviations missing
RELATED WORK
MOTIVATION
DEMONSTRATION EXAMPLE
A PLL circuit with a filter parameter uncertainty
Used filter block:
Two design requirements verified:
  lock time of the PLL to switch from one frequency to 1% of another frequency must not be higher than 1 ms
  an overshoot of the PLL output frequency f0 must be lower than 20%
AAF+A assertion for requirements description:
CONCLUSION AND FUTURE WORK
Online property verification of systems with parameter deviations
Specification violation-simulation run stopped
Check the method efficiency on complex systems
AFFINE ARITHMETIC
Parameter deviations modeled as ranges superimposed to nominal behavior x0
Ranges labeled by symbols
Symbols εi represent intervals [-1 1]
xi -numerical value which scales the interval
Assertion-based approach combined with Affine Arithmetic
Combination of high coverage of formal methods with high applicability of simulations to complex systems
[1] R.Y. Rubinstein, Simulation and the Monte Carlo method, John Wiley&Sons, New York, USA, 1981.
[2] M. Rafaila, C. Grimm, C. Decker, and G. Pelz, “Sequential design of experiments for effective model-based validation of electronic control units,’’e&I Elektrotechnik und Informationstechnik, vol. 127, pp. 164-170, 2010.
[3] W. Hartong, L. Hedrich, and E. Barke, “On discrete modeling and model checking of nonlinear analog systems’’, CAV ‘02, pp. 401-413, 2002.
[4] D. Nickovic, and O. Maler, “AMT: A Property-Based Monitoring Tool for Analog Systems”, FORMATS 2007, pp. 304-319, 2007.
[5] S. Lämmermann, A. Jesser, M. Rathgeber, J. Ruf, L. Hedrich, T. Kropf, and W. Rosenstiel, “Checking Heterogeneous Signal Characteristics Applying Assertion-Based Verification,’’ Frontiers in Analog Circuit Verification FAC, 2009.
[6] S. Steinhorst, A. Jesser, L.Hedrich, “Model Checking of Analog Systems using an Analog Specification Language”, DATE’08, pp. 324-329, 2008.
THE ASSERTION SYNTAX
REFERENCES
ASSERTION-BASED VERIFICATION WITH AFFINE ARITHMETIC
Design of Cyber-Physical Systems
Kaiserslautern Univerisity of Technology
(radojicic,grimm)@cs.uni-kl.de
Carna Radojicic
and Christoph Grimm
Assertion-based Verification of Phase-Locked Loop Circuit with Affine Arithmetic
The set of AAF+A comprised of two sets:
  TBF – verify properties in time domain
  FBF – verify properties in frequency domain
AAF+A assertions compressed into one using logic and, or and
imply operators:
Florian Schupfer and
Michael Rathmair
Institute of Computer Technology
Vienna Univerisity of Technology
(schupfer, rathmair)@ict.tuwien.ac.at
Multi run simulations
  Statistic Analysis – Monte Carlo simulations [1]
  Worst Case Analysis – Design of Experiments [2]
Formal verification methods [3] – state explosion problem for complex systems
Assertion-based techniques – verify only nominal system behavior
  Offline verification of analog systems properties – AMT Tool [4]
  Online verification of heterogeneous systems – MSA [5]
  Model checking combined with assertions – ASL [6]
EXPERIMENTAL RESULTS
The PLL was simulated in SystemC AMS for 100s with the sampling rate Ts=0,1ms
The Assertion 1 was satisfied and simulation run passed
The verification process consumed additional simulation time of only 1.7s